## Slide 1
Figure S1
Figure S1. Components (A-E) and units (F-H) for constructing electric field screens. (A) Negative or positive voltage generator with two terminals (T1, T2) for connection to a grounded line and a conductor to be charged. (B) Grounded line connected to a voltage generator and a metal net. (C) A layer of insulated metal wires arranged horizontally at specific intervals and interconnected. (D) Metal net. (E) Polypropylene frame (insulator). (F) Metal-wire unit, consisting of a layer of insulated metal wires fixed within a frame and connected to a negative or positive voltage generator. (G) Metal-net unit linked to a negative voltage generator. (H) Metal-net unit linked to a grounded line.